## Slide 1: Lab1: Design an 8-bit Subtractor
National Chiao Tung University
Chun-Jen Tsai
9/18/2015

## Slide 2: Lab 1: Design an 8-bit Subtractor
Through this lab, you will learn how to use the EDA tool for this course
  Please read the tutorial, dlb15_Intro_to_EDA_Tools.pdf, by yourself and start practicing in the lab
  You should review your old textbook on Digital Circuit Design by Mano to get a feel of the Verilog HDL
Lab target: design an 8-bit subtractor and use ISim to verify that your design is correct
  You must demo to your TA BEFORE 9/28 that your circuit works well and that you know how to use the CAD tool for simulation

## Slide 3: Design of an 8-bit Subtractor
An 8-bit subtractor can be constructed by a circuit module that computes the two’s complement of the subtrahend and add it to the minuend
  In the tutorial, dlb15_Intro_to_ EDA_Tools.pdf, you have learned how to design a 4-bit full adder
Your subtractor should have two 8-bit input ports and one 9-bit output port
  Any negative numbers are in 2’s complement
Only gate-level operators are allowed, see next slide
You must design your own testbench to make sure your logic works. At demo time, the TA will ask you to add extra test patterns to your testbench

## Slide 4: Gate-Level Operators Only, Please
You cannot use high-level (RTL-level) operators such as “complement”, “negative”, or even “subtraction” operators in your design
For 2’s complement, you can use the logic diagram as follows (I’s are input bits, O’s are output bits):
0
I0
O0
I1
O1
I2
O2
I3
O3
C
logic diagram of 4-bit 2’s complement