## Slide 1: Lab3: Push Buttons and LED Control
National Chiao Tung University
Chun-Jen Tsai
10/10/2015

## Slide 2: Lab 3: Push Buttons and LED Control
In this lab, you will use the Spartan-3E board to implement a simple I/O control circuit
  There are 5 push-buttons and 8 LED lights on the board
  You must design a synchronous circuit that reads the push-button inputs and use the inputs to increase/decrease the value of a 4-bit counter
  You must display the counter value using the 8 LEDs in sign-extended 2’s complement binary format at any time
You will demo the design to your TA during the lab hours on 10/19

## Slide 3: Buttons and LEDs on the Board
The Spartan-3E Starter Kit
LEDs
Push Buttons

## Slide 4: The System Behavior of Lab3
Your circuit has a 4-bit counter register
  The counter value is set to zero upon reset
  The counter value is in 2’complement from –8 ~ 7
Two push-buttons are used to increase/decrease the counter:
  Push the west/east buttons increase/decrease the counter by 1
  If the counter value becomes grater than 7, it is truncated to 7; if the value is smaller than –8, it is set to –8
The south button is used to reset the counter to zero
The counter register value will be displayed in sign-extended binary format using the 8 LEDs at any time

## Slide 5: Push buttons and LEDs Control
Use the LED lights to display the value of the counter register:
“on” means “1” and “off” means “0”. The most significant bit is LD7.
Counter + 1
Counter reset
Counter – 1
When a push button is pressed, the following actions is applied to the counter register:

## Slide 6: User I/O Pins of an FPGA IC
There are many “FPGA” pins that are used as user I/O pins: each pin connects to an I/O device such as the push-buttons or the LEDs:
Bottom-view of an FPGA IC (shows IC pins)
Top-view of an FPGA IC (shows IC markings)

## Slide 7: FPGA Pin Coordinates
Each pin at the bottom of the FPGA has a coordinate. For example, “K17” is the coordinate of the red pin of our Spartan-3E IC:
K17

## Slide 8: Use the I/O Pin Signal in Verilog
To read/write the I/O pins, we must map the pin coordinates to Verilog signals in our code
  User constraints are used to do the job
A user constraint is a text command that specifies the physical property in an HDL code. For example, for the four push-buttons, their mapping to Verilog signals can be as follows:
NET "BTN_EAST" LOC = "H13" | IOSTANDARD = LVTTL | PULLDOWN;
NET "BTN_NORTH" LOC = "V4" | IOSTANDARD = LVTTL | PULLDOWN;
NET "BTN_SOUTH" LOC = "K17" | IOSTANDARD = LVTTL | PULLDOWN;
NET "BTN_WEST" LOC = "D18" | IOSTANDARD = LVTTL | PULLDOWN;
Signal names to be used in your Verilog code!
IC pin coordinates
Signal type
Signal property

## Slide 9: How to Read the Input Push-Button
The physical connection from an FPGA I/O pin to a push-button is as follows:
Ideally, when a push-button is pushed (the circuit is closed), the FPGA pin that connects to the button becomes high voltage and the corresponding signal in Verilog reads “1”, otherwise it reads “0”.
A pull-down resister
A buffer gate of the I/O pin

## Slide 10: The Bouncing Problem
In reality, however, the signal value oscillates between 0 and 1 several times before it stabilizes. This is called the bouncing behavior of a hardware button.
The actual digital signal:
The physical voltage values:
time
voltage
time
Signal value
button off
button on
button pressed
Logic “low”
Logic “high”
Logic threshold
button bouncing period

## Slide 11: The De-bouncing Circuit
To detect whether the button has been pressed, you cannot simply check the button signals:
  This circuit will catch all the state changes during the bouncing period  a single button click will be treated as multiple clicks!
You must find a way to average-out the noises of the push-button signal during the bouncing period
  Hint: you can use a shift register to accumulate the input signal; or a timer to wait out the bouncing period
always @(posedge clk, posedge reset) if (reset == 1)
button_north_is_pressed = 0;
else
button_north_is_pressed = (BTN_NORTH)? 1 : 0;

## Slide 12: Turn On/Off the LEDs
The LEDs can be turned on or off by writing 1 or 0 to the corresponding Verilog signals (reg [7:0] LED):
NET "LED[7]" LOC = "F9" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[6]" LOC = "E9" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[5]" LOC = "D11" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[4]" LOC = "C11" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[3]" LOC = "F11" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[2]" LOC = "E11" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[1]" LOC = "E12" | IOSTANDARD = LVTTL | DRIVE = 8;
NET "LED[0]" LOC = "F12" | IOSTANDARD = LVTTL | DRIVE = 8;
LED[?]
FPGA I/O Pin
LED light

## Slide 13: Clock and Reset Pins
For synchronous design, you need a clock signal for your circuit
  The clock signal usually comes from an on-board oscillator
  There is an FPGA pin that connects to the oscillator
For the Spartan-3E Starter board, the south push-button (K17) is used as the reset pin
  The reset pin is connected to an active de-bouncing IC so you do not have to de-bounce its input!
NET "CLK" LOC = "C9" | IOSTANDARD = LVCMOS33;
# Define clock period for 50 MHz oscillator
NET "CLK" PERIOD = 20.0ns HIGH 40%;

## Slide 14: Create ISE Projects for the Board
As before, we create a new ISE project:

## Slide 15: Specify I/O Ports
But this time, we specify the I/O ports of the module as follows:

## Slide 16: Create User Constraints
Select “I/O Pin Planning” to create user constraints:

## Slide 17: The User Constraint Editor
Assign the Verilog I/O ports to pin coordinates:

## Slide 18: Adding Clock Signal Constraints (1/2)
Now, the signal “clk” has a default timing constraint, we can modify it once the design is ready for synthesis:

## Slide 19: Adding Clock Signal Constraints (2/2)
The default constraint should work fine, but we can change the duty cycle to better match the board

## Slide 20: Generate the Programming File
Now, create the programming file “lab3.bit” for FPGA:
double-click this to generate *.bit file
double-click this to run the iMPACT tool

## Slide 21: Downloading Your Circuit to the Board
To download your programming file into the FPGA, you must run the “iMPACT” tool:

## Slide 22: Detect the FPGA from iMPACT
Power on the board and initialize the JTAG chain:

## Slide 23: Assign the *.bit File to the FPGA
JTAG shows three IC’s, we only use the first one:

## Slide 24: Browse to the *.bit File
Browse to your directory and select the bit file for Lab3:

## Slide 25: Skip Configuration from SPI ROM
We do not use the SPI flash to configure the FPGA

## Slide 26: Bypass the Next Two IC’s
The next two IC’s in the JTAG chain are special flash memory  they are obsolete, bypass next two boxes!

## Slide 27: Program the FPGA
Finally, we can right-click the green IC to program it!

## Slide 28: Test Your Design
You can now test your circuit by clicking the buttons:

## Slide 29: Reference
Xilinx, Spartan-3E Starter Kit Board User Guide, UG230 (v1.0), March 9, 2006. Available from: http://www.xilinx.com/support/documentation/boards_and_kits/ug230.pdf