## Slide 1: Lab2: Design a Postfix Calculator
National Chiao Tung University
Chun-Jen Tsai
9/25/2015

## Slide 2: Lab 2: Design a Postfix Calculator
In this lab, you will design a postfix calculator and use the ISE simulator to evaluate its correctness
  The postfix calculator has an 4-bit input port that input a 4-bit operand or a 4-bit operator per clock cycle
  The postfix calculator has an internal stack memory that stores operands and temporary results
  The calculator only supports three operand +, –, 
  The expression has no more than 8 operands
You will demo to your TA during the lab hours on 10/21 or 10/28
  The testbench postfix_tb.v can be used to test your design

## Slide 3: Postfix Expression
In normal arithmetic expressions, we put operator in between two operands, for example, 2 + 7. This is called infix expression
For postfix expression, the operator is written behind the operands, for example, the infix expression “2 + 7” is written as “2 7 +” in postfix notation
For long expressions, postfix notation does not require parentheses for computation precedence, for example, “(2 + 7)  5” can be written as “2 7 + 5 ”

## Slide 4: Postfix Computation
A postfix expression is usually computed with the help of a stack storage using the following rules
  If an operand is read from the input string, push it to the stack
  If an operator is read from the input string, pop two operands from the stack and perform the computation, the result is push back to the stack
For example, to compute 2 7 + 5 
Input: 2
2
stack
Input: 7
2
stack
7
Input: +
9
stack
Input: 5
9
stack
5
Input: 
45
stack
Output: 45
stack

## Slide 5: Module Specification (1/2)
Module name: postfix
I/O ports:
  Input ports: CLK, RESET, OP_MODE, IN_VALID, IN[3:0]
  Output ports: OUT[15:0], OUT_VALID
CLK is the clock signal for synchronous design
  All signals are sampled at the positive edge of CLK
RESET is the asynchronous, active low reset signal
OP_MODE is high if IN[3:0] is an operator; low if IN[3:0] is an operand
IN_VALID is high when IN[3:0] has valid input
  High-to-low transition of IN_VALID signals the end of the input

## Slide 6: Module Specification (2/2)
When OP_MODE is high, the operator code of IN[3:0] is as follows:
OUT[15:0] is a signed integer in two’s complement
OUT_VALID is high when the result is in OUT[15:0]
OUT_VALID should go high in less than three cycles after IN_VALID becomes low
IN[3:0] when OP_MODE == 1’b1 | Operator
0001 | +
0010 | –
0100 | 

## Slide 7: Timing Diagram
The timing diagram of the sample input 2 7 + 5 * is as follows:
CLK
IN_VALID
IN[3:0]
2
7
OUT[15:0]
OUT_VALID
5 cycles
OP_MODE
+
5

45
RESET
0